Battery Monitor
Final Report

Automatio- ja systeemitekniikan projektityöt
AS-0.3200
Spring 2014

Otso Jousimaa
Aleksi Salonen
Johan Holmberg
25.5.2014

# Abbreviations
ADC	- Analog to Digital Converter
BOM	- Bill Of Materials
CS	- SPI Chip Select
ESD	- Electrostatic Discharge
KCL	- Kirchoff's Current Law
LPP	- Low-Pass Filtering
MBPS	- Megabits Per Second
MCU	- ????????????????????????????????????????????????????????????????
MISO	- SPI Master In, Slave Out
MOSI	- SPI Master Out, Slave In
SCLK	- SPI Clock
SMPS	- ????????????????????????????????????????????????????????????????
SPI	- Serial Peripheral Interface bus
TTL	- Transistor-Transistor logic
USB	- Universal Serial Bus
# 1 Introduction
The original project task was to create a battery balancer solution for the batteries in an electric car. The solution would consist of a separate battery balancer board, battery monitor board and a controller that would command the circuits. The battery balancer was designed and produced in another project during the Autumn of 2013. This project was concentrated on designing and producing the monitor part and integrating all the components into a working system.
Due to the fact that the balancer boards from the previous project were broken, the project scope was reduced to designing and producing the monitor board and controlling the monitor with a microcontroller. This document describes the final solution to the updated task. We also thought about making our own balancer board, but as there were no blueprints from the previous group, we deemed it to be way too time consuming. Also, the ordering process would've taken over 2 weeks, and there wouldn't have been time to write any software to use the balancer board.
The monitor board was designed using KiCad. There was enough components to fit on the board to motivate the use of a 4 layer board and KiCad capabilities to design multilayered boards. Also, as the boards were ordered from China instead of producing them on our own, we had no real reason not to use the 4 layer board.
To make the task easier, we chose to use a Arduino Nano board with its ATmega328 microcontroller to run the necessary monitoring logic. The Arduino environment is easy to set up, which allowed us to put more focus on designing the monitor board and writing software for controlling the board.
MORE INTRODUCTION HERE!

# 2 Workflow
## 2.1 Study phase
Immediately at the beginning of the project we stumbled upon problems. We could not get the balancer board from the previous project to work. It took a while before we got to the root of the problem. Some pins of the main circuit on the board were short circuited. We were unable to fix the short circuited pins which lead to the updated project scope as mentioned in the introduction. Also, even if we could've removed the short circuits, the board probably wouldn't have worked. It's possible, that during the short circuit removal attempts the board overheated and broke some components. The other board was broken before we got it, as there were visible burn marks in some of it's components.
We also had to study on how to use KiCad. Luckily, Otso had prior experience and was willing to teach us about the software.

## 2.2 Initial design
As mentioned in the introduction, we decided to use the 4 layer board design, as this was supported by KiCad and it made the board design a lot more easier. 4-layer PCB is stacked up with non-critical signals in the bottom, then power planes, then ground and on top are sensitive and high impedance signals. We used a few simple design rules: Components are placed on top side in a 1.27 mm grid and orientated in right angles. As for the board itself, there should be no buried or blind vias. Also, PCB traces use 45 degree turns and are centered to pads.
Isolation boundary was also deemed necessary, since in case of overvoltage the board would likely fry the microcontroller and the pc that's attached to the microcontroller. In the planned usage the batteries would produce 50 V and the standard USB can take only 5V. That's why the isolation boundary limits the voltage to 5V all the time.

## 2.3 Producing the boards
Because it is too difficult to produce your own 4 layered board, the monitor boards were ordered from China. The components on the board were soldered by hand. We also created a stripped version of the board as a 2 layered design and tried to solder it, but soon realized that the quality was not good enough for precision soldering.

## 2.4 Software development
The Arduino development environment was tested early on and some test programs were written to ensure that the Arduino with its ATmega328 was suited for the job.
Serious software development began in the beginning of April. This was already far behind schedule. Software development was rapid and quite straight forward, with a few major problems. One problem was that when adding code at some certain points, the Arduino would crash and reboot, or just stop communicating with any computer over the serial bus. The Arduino environment also had previously unknown restrictions which forced the team to modify the software architecture several times.

## 2.5 Documentation

# 3 Project results
## 3.1 Hardware

## 3.2 Software
### 3.2.1 Software structure and interfaces
The intended structure of the software is depicted in Figure 1 below.
Figure 1 Software components and interfaces

Battery
Battery
Battery
Battery
Monitor
Balancer
Microcontroller

Self Test
SPI
I/O
Logic
DB

SPI
Bus

Serial
I/O
PC

As seen in Figure 1 above, the software is split into several modules to keep the code structure clear. The Logic module consists of the main loop, which makes various checks and schedules the microcontrollers operation. The Serial I/O module is responsible for handling user input to the system. The SPI I/O module handles sending and receiving data to and from the SPI bus. The Database (DB) module is intended to store data from the monitor and balancer boards in meaningful structures for the Logic modules purposes. Lastly, the Self Test module checks incoming data from the SPI bus as well as the microcontrollers internal data and checks that the entire system operates properly. It raises error flags which the Logic module can use in case of invalid operation.
The software is configured from a laptop connected to the microcontroller over a serial port. In the case of the Arduino Nano board we used, this simply means installing the Arduino development environment and connecting the computer to the Arduino over USB. Using the Arduino Serial Monitor feature, the user can send commands to the microcontroller.
The microcontroller controls the monitor board over a SPI bus. This is done by writing to control registers in the monitors LTC6803 circuit. Data is read from the circuit by reading control or diagnostics registers on the LTC6803.
The balancer board has not been done yet and is therefore marked with red in Figure 1.

### 3.2.2 Software design
The software is designed to be modular so that it can be modified and improved later. The design is illustrated below in Figure 2.

Figure 2 Software design
Logic - main

========
Definitions &
Global data

main
balancerLogic
Microcontroller
SPI I/O

spi_io
Serial I/O

handleInput
pec
printData
Self Test

Database

db

## 3.3 Interfaces
### 3.3.1 Monitor – Microcontroller
The LTC6803-3 communicates over SPI with controller.

### 3.3.2 Monitor – Batteries

### 3.3.3 Microcontroller – PC
The ATmega328 on the Arduino Nano communicates with a PC over a Serial Port with speed 9600bps.

## 3.4 Implemented features and usage????????
# 4 Time usage and schedule
The original schedule for the project can be seen below.

We were able to stick to the project schedule the first weeks, almost up until the intermediate report. Due to other courses, we fell significantly behind schedule after the intermediate report. The hardware part of the project progressed far more smoothly than the software. The software was developed mainly during the last 4 weeks of the project. Team member time usage per week can be seen below.

Week
Hours
# 5 Future work and improvement suggestions

# References