# Design Guidelines for AS-0.3200 Battery balancer project
# Introduction
This document outlines the design practices used in this project.The goal is to get a consistent look and feel in project.
The design guidelines also are a sanity check for design choices. It is hard to do horrible mistakes with these guidelines, and any exception should be well thought out and reasoned.
“Autorouter did it” is not a reason for a design choice.
# PCB Layout
## Layer stackup
### 2-Layer PCB
Top is signal and bottom is groundplane. Groundplane can be used for jumping, as long as return path of critical signals isn't cut off.
### 4-Layer PCB
Top: Sensitive and high impedance signals.
1st inner: Ground
2nd inner: Power planes, high current..
Bottom: Non-critical signals.
## Traces
Traces are minimum of 0.245 mm / 9 mil thick. This allows for SSOP-packaged IC with rounding errors. Minimum isolation is also 0.245 mm / 9 mil. 0.5 mm / 20 mil traces are preferred.
## Vias
### 2-Layer boards
2-Layer boards are manufactured by hand. This means:
As few vias as possible. You are going to solder them by hand.
No vias under components.
2 mm dia pad with 1 mm drill is preferred.
1.2 mm dia pad with 0.6 mm drill is possible.
### 4-Layer boards
4-Layer boards are manufactured at factory.
No buried or blind vias.
## Grids
### Component placement
Componets are placed on top side.
Components are placed on a 1.27 mm / 50 mil grid.
Componets are oriented in right angles.
### PCB Trace placement
PCB traces are centered to pads.
PCB traces enter pad at right angle.
PCB traces use 45 degree turns.

# Component selection
## Passives
Passives are 0805 packaged whenever possible.
## Diodes – not including leds
Diodes are in SMB / DO-214AA package whenever possible.
## Discrete transistors – including fets
Package is SOT323 / SC-70 whenever practical.
Pin order is BCE / GDS.

## Connectors
For low currents (<1 A) 2.54 mm pitched locking connectors are used.
Example:
http://www.taydaelectronics.com/connectors-sockets/wafer-housing-crimp-terminal/serie-2500-2-54mm/housing-connector-2-54mm-2-pins.html
http://www.taydaelectronics.com/connectors-sockets/wafer-housing-crimp-terminal/serie-2500-2-54mm/wafer-connector-2-54mm-2-pins-right-angle.html
http://www.taydaelectronics.com/connectors-sockets/wafer-housing-crimp-terminal/serie-2500-2-54mm/crimp-terminal-connector-2-54mm.html

For higher currents 5.00 (NOT 5.08) pitched screw terminals are used.
Example:
http://www.taydaelectronics.com/connectors-sockets/terminal-blocks/pcb-mount/dg128-screw-terminal-block-2-positions-5mm.html